RealTimeController(DS1337)

20131108
This use i2c_rd and i2c_wr.

Reference;
DS1337_1.3.f

Connection
   RTC DS1337 Propeller
        scl ---- P28
        sda ---- P29
        INTA ---- n LED p --- 220ohm -- 3.3V
   SQW/INTB ---- n LED p --- 220ohm – 3.3V

--- Display register value
Prop0 Cog6 ok
disp_reg
Address(hex) value(hex)
        00 33
        01 03
        02 00
        03 01
        04 01
        05 01
        06 00
        07 00
        08 00
        09 00
        0A 00
        0B 00
        0C 00
        0D 00
        0E 18
        0F 80
Prop0 Cog6 ok

Set 24Hour-mode/Date on current/alarm1/alarm2 by set_current
--- Set current-time to 2013/11/5 TUE 20:28:00
2013 11 5 2 20 28 set_current

CurrentTime
Year: 2013
Date: NOV 5 TUE
Time: 20:28:00
Prop0 Cog6 ok
Week is defined by 'rtc_week'.

--- Set alarm1 to [Date]5 20:30:00
5 20 30 set_alm1

Alarm1 setting
Date: 5
Time: 20:30:00

Alarm1 Interupt:Enabled
Alarm2 Interupt:Disabled
Prop0 Cog6 ok

--- Set alarm2 to [Date]2 20:33
2 20 33 set_alm2

Alarm2 setting
Date: 2
Time: 20:33

Alarm1 Interupt:Enabled
Alarm2 Interupt:Enabled
Prop0 Cog6 ok

--- Check alarm1/alarm2 flag
chk_INT
Alarm1 Flag:0
Alarm2 Flag:0

Prop0 Cog6 ok

--- Display all setting
all

CurrentTime
Year: 2013
Date: NOV 5 TUE
Time: 20:29:01

Alarm1 setting
Date: 5
Time: 20:30:00

Alarm2 setting
Date: 2
Time: 20:33
Prop0 Cog6 ok
--- Change alarm2 to week of day
1 alarm2 alm_Day
Prop0 Cog6 ok

--- Display all setting
all

CurrentTime
Year: 2013
Date: NOV 5 TUE
Time: 20:29:14

Alarm1 setting
Date: 5
Time: 20:30:00

Alarm2 setting
Week: TUE
Time: 20:33

Prop0 Cog6 ok

INTA-pin goes to Low at 20:30 11/5 TUE
--- Check alarm1/alarm2 flag
chk_INT
Alarm1 Flag:1
Alarm2 Flag:0

Prop0 Cog6 ok

INTA-pin goes to Hi
--- Clear INT-flag for alarm1
alarm1 clr_INT
Alarm1 Flag:0
Alarm2 Flag:0

Prop0 Cog6 ok

INTA-pin goes to Low at 20:33 11/5 TUE
--- Check alarm1/alarm2 flag
chk_INT
Alarm1 Flag:0
Alarm2 Flag:1
Prop0 Cog6 ok
INTA-pin goes to Hi
--- Clear INT-flag for alarm2
alarm2 clr_INT
Alarm1 Flag:0
Alarm2 Flag:0

Prop0 Cog6 ok

--- Set INTCN because of using SQW/INTB-pin
1 set_INTCN
Prop0 Cog6 ok

--- Set alarm2 to Tue 20:36
2 20 36 set_alm2

Alarm2 setting
Week: TUE
Time: 20:36

Alarm1 Interupt:Enabled
Alarm2 Interupt:Enabled
Prop0 Cog6 ok
--- Set alarm2 to [No Day/Date]
1 alarm2 no_DY/DT
Prop0 Cog6 ok

--- Display all setting
all

CurrentTime
Year: 2013
Date: NOV 5 TUE
Time: 20:34:26

Alarm1 setting
Date: 5
Time: 20:30:00

Alarm2 setting
Time: 20:36

Prop0 Cog6 ok

SQW/INTB-pin goes to Low at 21:10
--- Check alarm1/alarm2 flag
chk_INT
Alarm1 Flag:0
Alarm2 Flag:1

Prop0 Cog6 ok

--- Clear INT-flag for alarm1
alarm2 clr_INT
Alarm1 Flag:0
Alarm2 Flag:0

Prop0 Cog6 ok

--- Back alarm2 to [Date]
0 alarm2 no_DY/DT
Prop0 Cog6 ok
all

CurrentTime
Year: 2013
Date: NOV 5 TUE
Time: 20:36:50

Alarm1 setting
Date: 5
Time: 20:30:00

Alarm2 setting
Week: TUE
Time: 20:36

Prop0 Cog6 ok

Set current/alarm1/alarm2 to 12Hour-mode
1 set_12H

CurrentTime
Year: 2013
Date: NOV 5 TUE
Time: PM 08:37:05

Alarm1 setting
Date: 5
Time: PM 08:30:00

Alarm2 setting
Week: TUE
Time: PM 08:36

Prop0 Cog6 ok

--- Set alarm1 to [Date]5 20:40:00
5 20 40 set_alm1

Alarm1 setting
Date: 5
Time: PM 08:40:00

Alarm1 Interupt:Enabled
Alarm2 Interupt:Enabled
Prop0 Cog6 ok

--- Display all setting
all

CurrentTime
Year: 2013
Date: NOV 5 TUE
Time: PM 08:38:06

Alarm1 setting
Date: 5
Time: PM 08:40:00

Alarm2 setting
Week: TUE
Time: PM 08:36

Prop0 Cog6 ok
INTA-pin goes to Low at 20:40
--- Check alarm1/alarm2 flag
chk_INT
Alarm1 Flag:1
Alarm2 Flag:0

Prop0 Cog6 ok

 INTA-pin goes to Hi
--- Clear INT-flag for alarm1
alarm1 clr_INT
Alarm1 Flag:0
Alarm2 Flag:0

Prop0 Cog6 ok

--- Check INTCN
control DS1337 i2c_rd hex st? sc
ST: 0000_001F 0000_0000
2 items cleared
Prop0 Cog6 ok
--- Clear INTCN
0 set_INTCN
Prop0 Cog6 ok
control DS1337 i2c_rd st? sc
control DS1337 i2c_rd st? sc
ST: 0000_001B 0000_0000
2 items cleared
Prop0 Cog6 ok

--- output 8.192kHz from SQW/INTB-pin (default is 32.768kHz) ---
8kHz set_SQW
Prop0 Cog6 ok
--- output 4.096kHz from SQW/INTB-pin ---
4kHz set_SQW
Prop0 Cog6 ok
--- output 32.768kHz from SQW/INTB-pin ---
32kHz set_SQW
32kHz set_SQW
Prop0 Cog6 ok
--- output 1Hz from SQW/INTB-pin ---
1Hz set_SQW
Prop0 Cog6 ok

--- When osc stop, DS1337's clock stop ---
-- 1Hz blinking stop
0 osc_on/off
Prop0 Cog6 ok
--- Re-start DS1337's clock ---
-- 1Hz blinking re-start
1 osc_on/off
Prop0 Cog6 ok