Frequently Used Code

2013/9/29 20160107
Print out to TeraTerm
word' . ' print out figure from 0 to FFFFFFFF
And it follow space.
Control-code(for example TAB=9) is ignore.
If you don't add space, you can use word'.byte/.word/.long'.

     Prop0 Cog6 ok
     hex
     Prop0 Cog6 ok
     0 .
     0 Prop0 Cog6 ok
     9 .
     9 Prop0 Cog6 ok
     FFFFFFFF .
     -1 Prop0 Cog6 ok
     9 .byte
     09Prop0 Cog6 ok
     FFFFFFFF .byte
     FFProp0 Cog6 ok
     FFFFFFFF .long
     FFFF_FFFFProp0 Cog6 ok

Word'emit' print out character-code.
This is used for printing character.
Control-code also print out.
And space is not added.
Printed characters are depended on your PC's character-code.
Your system might not print out 'B1 emit'. Or different character.

     Prop0 Cog6 ok
     hex
     Prop0 Cog6 ok
     0 emit
     Prop0 Cog6 ok
     9 emit
     (TAB) Prop0 Cog6 ok
     30 emit
     0Prop0 Cog6 ok
     Prop0 Cog6 ok
     7D emit
     }Prop0 Cog6 ok
     7E emit
     ?Prop0 Cog6 ok
     7F emit
     Prop0 Cog6 ok
     A1 emit
     ｡Prop0 Cog6 ok
     B1 emit
     ｱProp0 Cog6 ok

Definition of port
Defining port to OUT/IN
Using 'wconstant '

     0 wconstant DATA
     1 wconstant SCLK
     2 wconstant LCLK
     3 wconstant IN

Defining input-port's mask
Using 'constant'
It can use wconstant if port is from P0 to P15

     IN >m constant INm

WORD-definition set up each out-port to hi/lo
     : data_l DATA pinlo ;
     : data_h DATA pinhi ;
     : sclk_l SCLK pinlo ;
     : sclk_h SCLK pinhi ;
     : lclk_l LCLK pinlo ;
     : lclk_h LCLK pinhi ;

Set port to OUT
(Default: Port is IN Status on output-port is Low)
     : setup DATA 3 0 do dup pinout 1+ loop drop ;

Variable
variable for Long(4 bytes)
variable name
variable for word(2bytes)
wvariable name

Constant
constant for Long(4 bytes)
h12345678 constant name
constant for word(2bytes)
h1234 wconstant name
sample1 define 2 word constant(h1234 and hCCCC).
“-4 allot” roll back memory because sample1 have 4byte by variable
variable sample1 -4 allot h1234 w, hCCCC w,
wvariable sample2 -2 allot h12345678 l, hCCCCDDDD l,

Array
Array below are both 10bytes.
wvariable array1 8 allot
variable array2 6 allot

When definition of wvariable, array1 already occupy 2byte.
By using 8 allot, it add 8bytes.

Breaking loop
Repeat-loop break by hitting any key
begin
- statement -
fkey? swap drop
until

Repeat-loop break by ESC-key
begin
- statement -
fkey?
if
h1B = if 1 else 0 then	\ ESC-key is h1B
else
drop 0
then
until

Case statement
No case-statement in PropForth.
But there is substitute.
In case of value1=1 or 2 or 3 or >3 below;
\ ( n1 n2 -- n1 t/f ) n1:integer n2;compared value t/f: t = matched
: case over = ;

\ (n1 -- ) n1:integer
: test
1 case
if
statement1
else 2 case
if
statement2
else 3 case
if
statement3
else
statement4
thens
drop
;

String
Case1
Using defined word when string is 2,3 pieces.

There is inside PropForthStartKernel.f.
: (version) c" PropForth v5.0 2012JAN09 14:30 0" ;
     Prop0 Cog6 ok
     (version) .cstr cr
     PropForth v5.0 2012JAN09 14:30 0
     Prop0 Cog6 ok

     Prop0 Cog6 ok
     hex
     Prop0 Cog6 ok
     (version) 40 dump

     0AC8 0040:
     0AC8: 20 50 72 6F 70 46 6F 72 74 68 20 76 35 2E 35 20 PropForth v5.5
     0AD8: 32 30 31 33 46 65 62 32 30 20 31 31 3A 33 30 20 2013Feb20 11:30
     0AE8: 30 00 61 00 BC 0A 84 70 72 6F 70 00 4F 00 B2 0A 0.a....prop.O...
     0AF8: EE 0A 87 76 65 72 73 69 6F 6E 4F 00 C8 0A FA 0A ...versionO.....
     Prop0 Cog6 ok
Case2

Using defined word when string's length is same.
: test
c" JANFEBMARAPRMAYJUNJULAUGSEPOCTNOVDEC"
1+ swap hC min 1 max 1- 3 u* +
3 0 do dup C@ emit 1+ loop drop
;

     Prop0 Cog6 ok
     2 test cr
     FEB
     Prop0 Cog6 ok

     Prop0 Cog6 ok
     hex
     Prop0 Cog6 ok
     words test
     NFA (Forth/Asm Immediate eXecute) Name
     44BE F test
     Prop0 Cog6 ok
     44BE 30 dump

     44BE 0030:
     44BE: 84 74 65 73 74 00 66 26 24 4A 41 4E 46 45 42 4D .test.f&$JANFEBM
     44CE: 41 52 41 50 52 4D 41 59 4A 55 4E 4A 55 4C 41 55 ARAPRMAYJUNJULAU
     44DE: 47 53 45 50 4F 43 54 4E 4F 56 44 45 43 00 A0 14 GSEPOCTNOVDEC...
     Prop0 Cog6 ok

Case3
Allocating strings when using many differnt length strings

Defining word store string
: s, parsenw dup C@ 1+ bounds dup rot2 do C@++ c, loop drop ;

Defining string
wvariable main -2 allot s, Input s, Output s, Collection s, Feature s, EndCollection
wvariable global -2 allot s, UsagePage s, LogicalMinimum s, LogicalMaximum
s, PhysicalMinimum s, PhysicalMaximum s, UnutExponent s, Unit s, ReportSize
s, ReportID s, ReportCount s, Push s, Pop
wvariable local -2 allot s, Usage s, UsageMinimum s, UsageMaximum
s, DesignatorIndex s, DesignatorMinimum s, StringIndex s, StringMinimum
s, StringMaximum s, Delimiter
wvariable Attribute -2 allot s, Data s, Constant s, Array s, Variable s, Absolute
s, Relative
wvariable Collection -2 allot s, Physical s, Application s, Logical s, Report
s, NamedArray s, UsageSwitch s, UsageModifier
wvariable UsagePage -2 allot s, Undefined s, Generic_Desktop_Controls
s, Simulation_Controls s, VR_Controls s, Sport_Controls
s, Game_Controls s, Generic_Device_Controls s, Keyboard/Keypad s, LEDs s, Button
s, Ordinal s, Telephony s, Consumer
wvariable Generic_Desktop_Page -2 allot s, Undefined s, Pointer s, Mouse s, Reserved s, Joystick s, Game_Pad s, Keyboard
s, Keypad s, Multi-axis_Controller s, X s, Y s, Z s, Rx s, Ry s, Rz s, Slider s, Dial
s, Wheel

Check inside memory
main 200 dump

4B82 0200:
4B82: 05 49 6E 70 75 74 06 4F 75 74 70 75 74 0A 43 6F .Input.Output.Co
4B92: 6C 6C 65 63 74 69 6F 6E 07 46 65 61 74 75 72 65 llection.Feature
4BA2: 0D 45 6E 64 43 6F 6C 6C 65 63 74 69 6F 6E 7A 4B .EndCollectionzK
4BB2: 86 67 6C 6F 62 61 6C 76 4F 00 09 55 73 61 67 65 .globalvO..Usage
4BC2: 50 61 67 65 0E 4C 6F 67 69 63 61 6C 4D 69 6E 69 Page.LogicalMini
4BD2: 6D 75 6D 0E 4C 6F 67 69 63 61 6C 4D 61 78 69 6D mum.LogicalMaxim
4BE2: 75 6D 0F 50 68 79 73 69 63 61 6C 4D 69 6E 69 6D um.PhysicalMinim
4BF2: 75 6D 0F 50 68 79 73 69 63 61 6C 4D 61 78 69 6D um.PhysicalMaxim
4C02: 75 6D 0C 55 6E 75 74 45 78 70 6F 6E 65 6E 74 04 um.UnutExponent.
4C12: 55 6E 69 74 0A 52 65 70 6F 72 74 53 69 7A 65 08 Unit.ReportSize.
4C22: 52 65 70 6F 72 74 49 44 0B 52 65 70 6F 72 74 43 ReportID.ReportC
4C32: 6F 75 6E 74 04 50 75 73 68 03 50 6F 70 20 B2 4B ount.Push.Pop .K
4C42: 85 6C 6F 63 61 6C 4F 00 05 55 73 61 67 65 0C 55 .localO..Usage.U
4C52: 73 61 67 65 4D 69 6E 69 6D 75 6D 0C 55 73 61 67 sageMinimum.Usag
4C62: 65 4D 61 78 69 6D 75 6D 0F 44 65 73 69 67 6E 61 eMaximum.Designa
4C72: 74 6F 72 49 6E 64 65 78 11 44 65 73 69 67 6E 61 torIndex.Designa
4C82: 74 6F 72 4D 69 6E 69 6D 75 6D 0B 53 74 72 69 6E torMinimum.Strin
4C92: 67 49 6E 64 65 78 0D 53 74 72 69 6E 67 4D 69 6E gIndex.StringMin
4CA2: 69 6D 75 6D 0D 53 74 72 69 6E 67 4D 61 78 69 6D imum.StringMaxim
4CB2: 75 6D 09 44 65 6C 69 6D 69 74 65 72 42 4C 89 41 um.DelimiterBL.A
4CC2: 74 74 72 69 62 75 74 65 4F 00 04 44 61 74 61 08 ttributeO..Data.
4CD2: 43 6F 6E 73 74 61 6E 74 05 41 72 72 61 79 08 56 Constant.Array.V
4CE2: 61 72 69 61 62 6C 65 08 41 62 73 6F 6C 75 74 65 ariable.Absolute
4CF2: 08 52 65 6C 61 74 69 76 65 61 C0 4C 8A 43 6F 6C .Relativea.L.Col
4D02: 6C 65 63 74 69 6F 6E 72 4F 00 08 50 68 79 73 69 lectionrO..Physi
4D12: 63 61 6C 0B 41 70 70 6C 69 63 61 74 69 6F 6E 07 cal.Application.
4D22: 4C 6F 67 69 63 61 6C 06 52 65 70 6F 72 74 0A 4E Logical.Report.N
4D32: 61 6D 65 64 41 72 72 61 79 0B 55 73 61 67 65 53 amedArray.UsageS
4D42: 77 69 74 63 68 0D 55 73 61 67 65 4D 6F 64 69 66 witch.UsageModif
4D52: 69 65 72 69 FE 4C 89 55 73 61 67 65 50 61 67 65 ieri.L.UsagePage
4D62: 4F 00 09 55 6E 64 65 66 69 6E 65 64 18 47 65 6E O..Undefined.Gen
4D72: 65 72 69 63 5F 44 65 73 6B 74 6F 70 5F 43 6F 6E eric_Desktop_Con
Prop0 Cog6 ok

Defining word printing out string
\ Print out string
\ ( n1 n2 -- ) n1:index(0,1,2,..,n) n2:string-array's address
: dispStr
swap dup 0 <>
if
0 do
        dup C@ + 1+
loop
else
drop
then
.cstr
;

Print out defined string by 's,'
: test 3 main dispStr cr ; \ Print out index=3 inside 'main' string-array

     Prop0 Cog6 ok
     test
     Feature
     Prop0 Cog6 ok

FONT

Reference:
Propeller Manual V1.2 Chapter1 Page31 - Page33
HydraGameDevManual-v1.0.1.pdf Chapter16 Page336 - Page338

Loading Font.f

ROM-font inside propeller is $8000-$BFFF(4096Longs).
1Block-size(including 2characters) is 128byte(32Longs).
All are 128locks(128 X 2characters).
2Character's column(horizon derection) length are 4byte(1Long).
Even character is even dots(b0,2,....b26,b28,b30).
Odd character is odd dots(b1,2,....b27,b29,b31).
2Character's row(vertical derection) length are 32.
Character is 16 X 32pixel.

Word'font1' display combined fonts(odd & even character).

There are "@" and "A" below; But it cannot see characters.
Prop0 Cog6 ok
font1

$9000
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 1 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 0 0 0 0 0
0 0 0 0 0 0 0 1 0 1 0 1 0 1 1 1 1 1 1 1 1 1 0 1 0 1 0 1 0 0 0 0
0 0 0 0 0 0 0 1 0 1 1 1 1 0 1 0 1 0 1 0 1 0 1 1 1 1 0 1 0 0 0 0
0 0 0 0 0 1 0 1 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 1 0 1 0 0
0 0 0 0 0 1 1 1 1 1 1 0 1 0 0 0 0 0 0 0 0 0 1 0 1 1 1 1 0 1 0 0
0 0 0 0 0 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 0 0
0 0 0 0 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 0 0
0 0 0 0 1 1 1 1 1 1 0 0 0 0 1 0 1 0 1 0 1 0 1 0 0 1 1 1 1 1 0 0
0 0 0 0 1 1 1 1 0 1 0 1 1 1 1 1 1 1 1 1 1 1 1 1 0 1 1 1 1 1 0 0
0 0 0 0 1 1 1 1 0 1 0 1 1 1 1 1 0 1 0 1 1 1 1 1 0 1 1 1 1 1 0 0
0 0 0 0 1 1 1 1 0 1 0 1 1 1 1 1 0 1 0 1 1 1 1 1 0 1 1 1 1 1 0 0
0 0 0 0 1 1 1 1 0 1 0 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 1 1 1 0 0
0 0 0 0 1 1 1 1 1 1 0 0 0 0 1 0 1 0 1 0 0 0 1 0 1 1 1 1 0 1 0 0
0 0 0 0 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 1 0 1 0 0
0 0 0 0 0 1 1 1 1 1 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 0 0
0 0 0 0 0 1 1 1 1 1 1 0 1 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 0 0
0 0 0 0 0 1 0 1 1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 1 1 0 1 0 0
0 0 0 0 0 1 0 1 0 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 1 0 1 0 1 0 0
0 0 0 0 0 1 0 1 0 1 0 0 0 0 1 0 1 0 1 0 1 0 0 0 0 1 0 1 0 1 0 0
0 0 0 0 0 1 0 1 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 1 0 1 0 0
0 0 0 0 0 1 0 1 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 0 1 0 1 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0

Word'font2' can watch a little bit even and odd character.
Prop0 Cog6 ok
font2

$9000

        # # # # #
        # # # # # # # # #
      # # # #!#!#!#!# # # #
      # #!#! ! ! ! ! !#!# #
    # #!#! ! ! ! ! ! ! !#!# #
    #!#!#! ! ! !#!# #
    #!#!#! !#!#!#
   !#!#!# #!#!#
   !#!#!# ! ! ! ! ! #!#!#
   !#!# # #!#!#!#!#!#!# #!#!#
   !#!# # #!#!# # #!#!# #!#!#
   !#!# # #!#!# # #!#!# #!#!#
   !#!# # ! ! ! ! ! ! !#!#!#
   !#!#!# ! ! ! ! !#!# #
   !#!#!# # # #
    #!#!#! #!#!#
    #!#!#! ! !#!#!#
    # #!#! ! ! ! ! ! ! !#!# #
    # # #! ! ! ! ! ! ! !# # #
    # # # ! ! ! ! # # #
    # # # # # #
    # # # # # #

Word'font3' Display even/odd character separately
Prop0 Cog6 ok
font3

$9000

      ****
    ********
   **********
  **** ***
  *** ***
 *** **
 *** ***** **
 ** ****** **
 ** ** ** **
 ** ** ** **
 ** *********
 *** *** ***
 ***
  *** **
  **** ***
   **********
    ********
      ****

     *****
   *********
  ***********
  *** ***
 *** ***
 *** ***
 *** ***
 *** ***
 *** ***
 *************
 *************
 *************
 *** ***
 *** ***
 *** ***
 *** ***
 *** ***
 *** ***
 *** ***
 *** ***
 *** ***
 *** ***

Operating on another cog
When operating code on another cog, cogID is pointed out;
: test 5 0 do i . loop ;
c" test" 5 cogx
Loading auto_cog.f
Automatically, cogID is assigned on demo5;

     Prop0 Cog6 ok
     auto_set_demo
     available cogID:5
     available cogID:4
     available cogID:3
     available cogID:2
     available cogID:1
     available cogID:0
     No free Cog
     Prop0 Cog6 ok

     cogID:0x60543210
     Cog:0 #io chan:1 RUNNING TEST-F
     Cog:1 #io chan:1 RUNNING TEST-E
     Cog:2 #io chan:1 RUNNING TEST-D
     Cog:3 #io chan:1 RUNNING TEST-C
     Cog:4 #io chan:1 RUNNING TEST-B
     Cog:5 #io chan:1 RUNNING TEST-A
     Cog:6 #io chan:1 PropForth v5.5 2013Feb20 11:30 0 6(0)->7(0)
     Cog:7 #io chan:1 SERIAL 7(0)->6(0)
     Prop0 Cog6 ok

     -- Reset specified cog
     Prop0 Cog6 ok
     1 cog_reset

     CON:Prop0 Cog1 RESET - last status: 0 ok

     Cog:0 #io chan:1 RUNNING TEST-F
     Cog:1 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:2 #io chan:1 RUNNING TEST-D
     Cog:3 #io chan:1 RUNNING TEST-C
     Cog:4 #io chan:1 RUNNING TEST-B
     Cog:5 #io chan:1 RUNNING TEST-A
     Cog:6 #io chan:1 PropForth v5.5 2013Feb20 11:30 0 6(0)->7(0)
     Cog:7 #io chan:1 SERIAL 7(0)->6(0)
     cogID:0x50054320
     Prop0 Cog6 ok

     4 cog_reset

     CON:Prop0 Cog4 RESET - last status: 0 ok

     Cog:0 #io chan:1 RUNNING TEST-F
     Cog:1 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:2 #io chan:1 RUNNING TEST-D
     Cog:3 #io chan:1 RUNNING TEST-C
     Cog:4 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:5 #io chan:1 RUNNING TEST-A
     Cog:6 #io chan:1 PropForth v5.5 2013Feb20 11:30 0 6(0)->7(0)
     Cog:7 #io chan:1 SERIAL 7(0)->6(0)
     cogID:0x40005320
     Prop0 Cog6 ok

     -- Display each cog's string
     0 cog_string
     RUNNING TEST-F
     Prop0 Cog6 ok
     1 cog_string
     PropForth v5.5 2013Feb20 11:30 0
     Prop0 Cog6 ok
     7 cog_string
     SERIAL
     Prop0 Cog6 ok

   -- Reset all cogs --
     all_cog_reset

     CON:Prop0 Cog0 RESET - last status: 0 ok

     CON:Prop0 Cog2 RESET - last status: 0 ok

     CON:Prop0 Cog3 RESET - last status: 0 ok

     CON:Prop0 Cog5 RESET - last status: 0 ok

     Cog:0 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:1 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:2 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:3 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:4 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:5 #io chan:1 PropForth v5.5 2013Feb20 11:30 0
     Cog:6 #io chan:1 PropForth v5.5 2013Feb20 11:30 0 6(0)->7(0)
     Cog:7 #io chan:1 SERIAL 7(0)->6(0)
     Prop0 Cog6 ok