PID Exercise

20160204

2_wire_charLCD_0.1.f
PID_Exercize_-0.1.f
PID1 folder include Processing files.

I wrote PID-code to refer site below;
http://brettbeauregard.com/blog/2011/04/improving-the-beginners-pid-introduction/

I think Forth-code is easy. (Not using assembler word)
Important thing is only PID-code.

Procedure

1 Loading 2_wire_charLCD_0.1.f and PID_Exercize_-0.1.f.
    Start PID1.pde inside PID1 folder.

2 Execute PID1_Exercize
   Start PID1.pde → Opened Processing-window

3 Click left-button inside Processing-window.

DC-Fan start to rotate.
Rotation-speed drawed inside Processing wibndow.
Default PID-parameters are setpoint:1400,Kp=300,Ki=50,Kd=10.

PID-parameters can be chenged by using 12-KeyPad.

  Setpoint is from 0 to 2500
  By pushing Enter-key, value is entered

  By pushing Cancel-key, next item is displayed.

  Kp is from 0 to 4095
  By pushing Enter-key, value is entered

  By pushing Cancel-key, next item is displayed.

  Ki is from 0 to 4095
  By pushing Enter-key, value is entered

  By pushing Cancel-key, next item is displayed.

  Kd is from 0 to 4095
  By pushing Enter-key, value is entered

  By pushing Cancel-key, next item is displayed.

  In case of Auto(PID-ON), Output(PWM signal) merely
  display.
  Output(PWM signal) can be changed under Manual
  (PID-OFF).
  Value is from 0 to 100.

  By pushing Enter-key, value is entered

  By pushing Cancel-key, next item is displayed.

   By pushing Enter-key, PID-parameters are adopted.

  By pushing Enter-key, value is entered

  By pushing Cancel-key, next item is displayed.

  By pushing Enter-key, mode change to “Manual
  (PID-OFF)”.
  Displaying “AUTO(PID-ON)”.
  Alterneting “Manual(PID-OFF)” and “AUTO(PID-ON”)

  By pushing Cancel-key, back to “Setpoint”

Changed setpoint to 1000

Changed setpoint to 2000

Changed to Manual(PID-OFF)